## Slide 1: Soil Mechanics
Prof. Krunoslav Minažek
Josip Juraj Strossmayer University of Osijek

## Slide 2: Contents
Soil formation
Basic physical soil properties
Soil classification
Index tests
Classification symbols

## Slide 3: Soil formation
DEGRADATION – DECOMPOSTION OF BASE ROCK
TRANSPORTATIN – BY WATER, WIND OR ICE
SEDIMENTATION (in water, influenced by chemystry, overburden)
MINERALOGYCAL COMPOSITION
HUMAN ACTIVITY
SOIL FORMATION – particles
    Honeycomb structure
    Fluffy structure
    Complex structure

## Slide 4: Transportation and sedimentation
Wind direction
Sand particles
erosion
alluvion
erosion
alluvion

## Slide 5: Minerals of sand and clay
Sand minerals
Clay minerals

## Slide 6: Particle associations and arrangements
Complexity of particle associations and arrangements
Influence on physical and mechanical soil properties

## Slide 7: Particle assemblage
Soil matrix is assembled as mixture of different type of soil particles
Influence on physical and mechanical soil properties

## Slide 8: Basic physical soil properties
Size and coposition of particles
    FINE GRAINED SOIL – COHESSIVE SOILS (clay and silt)
    COARSE GRAINED SOIL – NONCOHESIVE SOILS (sand and gravel)
    Relative porosity
    Void ratio
air
water
Solid particles

## Slide 9: Soil density
density (of naturally) moist soil:  = M/V,
soil dry density: d = Md/V,
density of solid particles: s = Md/Vc
where: M=mass of naturally moist soil sample,
V = volume of soil sample,
Md= mass of dry sample (equal to mass of soil particless =Mc)

## Slide 10: Determination of soil particles density

## Slide 11: Soil moisture content
soil moisture: w = Mv/Md = (M-Md)/Md
(note: moisture content is defined as ratio between mass of water and solid particles ie dried sample, and not the wet sample, sample is dried at 1050C for 16-24 hours in order to remove all unbound water)
Saturation ratio Sr = Vv / Vp
(Sr is often expressed as percentage, ie Sr=0,45, means Sr=45% that is 45% of pore volume is filled with water, sample with Sr=100% is completely saturated).

## Slide 12: Typical values
Porosity – clay, silt 0.4-0.7 (0.5)
Porosity – gravel , sand 0.2-0.4 (0.3)
Density – clay, silt 1.6 - 2 Mg/m3
Density – gravel, sand 1.8-2.2 Mg/m3
Solid particles density – all soils - 2,5-2,7 Mg/m3

## Slide 13: Soil granulometric content
(G) Gravel 60 – 2 mm (coarse, medium, fine)
(S) Sand 2 – 0,06 mm (coarse, medium, fine)
(M) Silt 0,06 – 0,002 mm
(C) Clay ispod 0,002 mm
(6-2 system )
Sieving – gravel and sand
Hydrmetric analysis -aerometer – clay and silt

## Slide 14: Sieving – gravel and sand
set of sieves of different apperture sizes positioned with larger size apertures above smaller ones,
sieves with sample poured at the upper sieve are shaked and mass of remains on every sieve is measued

## Slide 15: Hydrometric analysis– principle

## Slide 16: The hydrometric analysis procedure
% of particles, for each hydrometer reading
Calculate P - H = reading in the blurred sample,
B = reading in distilled water,
W = mass of soil sample
particle diameter with P% - for each
Hydrometer reading,
K = constant, L = length of hydrometer,
T = time in min.

## Slide 17
0 %
100%
GRAVEL
SAND
SILT
CLAY
Log D (particles diameter, mm)
60
2
0.06
0.002
Granulometric curve: percentages of mass of particles with different diameter in the sample total

## Slide 18: Example of granulometric curve
STONE
GRAVEL
SAND
SILT
CLAY
coarse
medium
fine
coarse
medium
fine
PARTICLE DIAMETER, d (mm)
Mass of particles with diameter less the d percentage (%)

## Slide 19: Silt and clay - consistency
Depends on natural moisture content, related to liquid and plastic limit:
Liquid limit WL
Plastic limit WP
Srinkage limit WS
solid_WS_semi-solid_WP _ plastic _ WL _ liquid

## Slide 20: Liquid limit determination
CASAGRANDE METHOD
FALL CONE METHOD

## Slide 21: Plastic limit determination
Rolling the soil by hand on glass base unitl crumbling at 3 mm diameter occurs.

## Slide 22: Shrinkage limit determination
SHRINKAGE LIMIT:
The mositure of the sample when further
Moisutre reduction does not results in
volume reduction
– several atempts during drying
and sample volume measurement

## Slide 23: Index parameters for cohessive soil
Plasticity index: Ip=wL-wP
Consistency index: Ic=(wL-w0)/Ip
Ic and consitency: < 0,25 – very soft;
0,25-0,50 – soft
    0,50-0,75 – firm, 0,75-1,0 – stiff
    > 1,0 – very stiff
    (ISO 14688)

## Slide 24: Index parameters – non cohessive soil
Relative density:
ID= (emax-e0)/(emax-emin)
emax=maximal porosity, emin=minimal porosity, eo= actual porosity (natural, insitu), min. and max. porosities are determined using lab. tests)
Correlation to relative density (ISO 14688):
  ID=0-0.15 - very loose
  ID=0.15-0.35 - loose
  ID=0.35-0.65 - medium dense
  ID=0.65-0.85 - dense
  ID=0.85-1.00 - very dense

## Slide 25: Soil Classification (USCS –ASTM D2487-6)
Noncohessive soil – gravel G, sand S
well-graduated – W, poor-graduated P
GW, GP, SW, SP
Cohessive soil – clay C, silt M
High plasticity, low plasticity
Plasticity chart: wl – Ip
CH, CL, MH, ML
Combinations noncohessive-cohessive soils: GW-GC, SP-SM...

## Slide 26: Classification of non cohessive soil
Noncohessive soils – well-graduated (W),
poor-graduated (P), uniformly-graduated (U).
0 %
100%
GRAVEL
SAND
SILT
CLAY
Log D (mm)
60
2
0.06
0.002

## Slide 27: Description of granulometric curve
Characteristic diameters for the description of the granulometric curve are: D10, D30, D60
The granulometric composition curve for noncohessive soil is characterized by the following parameters:
uniformity coefficient: Cu = D60 / D10,
coefficient of curvature: Cc = D302 / (D10xD60)
According to the shape of the curve, soil can be:
well-graduated - contains a wide range of grains of different diameters
        for gravel: Cu > 4, and 1 < Cc < 3
        for sand: Cu > 6, and 1 < Cc < 3
poorly-graduated - particles of some diameters are missing
uniformly graduated - not present in all classification systems - contains particles of predominantly narrow spectrum in diameter

## Slide 28: Soil classification – Cohessive soil (plasticity chart)

## Slide 31: USCS Classification - Summary

## Slide 32: ESCS classification (EN ISO 14688-2:2018)

## Slide 33: Field determination and classification
Field determination from bored soil core
Important for overall soil description – fresh sample from soil mass
Soil description: type of soil (predominant soil – estimate of granulometric content), plasticity, consistency, colour, gloss (waxy glow...), smell (, presence of organic content, particle shape, roundness

## Slide 34: References
Mitchell, J.K. and Soga, K. (2005) Fundamentals of Soil Behavior. 3rd Edition, John Wiley & Sons, Hoboken.
Engineering Properties of Soils Based on Laboratory Testing Prof. Krishna Reddy, UIC EXPERIMENT 6 GRAIN SIZE ANALYSIS (SIEVE AND HYDROMETER ANALYSIS
ASTM D 2487 – 06 Standard Practice for Classification of Soils for Engineering Purposes (Unified Soil Classification System)
EN ISO 14688-2:2018 Geotechnical investigation and testing - Identification and classification of soil – Part 2: Principles for a classification